## Slide 1
Tools for Managing & Troubleshooting
OSDP Deployments
John Nemerofsky, Sage Integration
Jon Uren, Cypress Integration Solutions
Jacob LeRoy, Cypress Integration Solutions

## Slide 2
3-4 minutes Intro speakers
10-15 minutes OSDP advantages—security, functionality, interoperability; case study
20 minutes OSDP system comparison & components, OSDP best practices & troubleshooting
5-6 minutes Wrapup, future developments (?OSDP I/O devices, credentials, PIV)
15 minutes Q&A

## Slide 4: Panel Members
John Nemerofsky, Chief Operating Officer, Sage Integration
Tony Diodato, Founder, President/CEO, Cypress Integration Solutions
Jacob LeRoy, Sr. Sales & Development Manager, Cypress Integration Solutions

## Slide 5: Why OSDP?
Notes: Many advantages over both Wiegand and proprietary protocols

## Slide 6: Why OSDP?
Because the current situation is like Vegas baby!
- Non-deterministic “protocols”
High risk ( known vulnerabilities )
Time to say goodbye to legacy protocols
Notes: Many advantages over both Wiegand and proprietary protocols

## Slide 7: Why OSDP?
Secure communication
- Secure Channel: Encryption & authentication
Supervision
Meets Infosec requirements
Notes: Security & supervision
2-way communication protocol for supervision, encryption and authentication

## Slide 8: Why OSDP?
Enhanced functionality
- Longer distances & multi-drop installations
Larger data formats & higher baud rates
Remote updates from panel
Notes: enhanced functionality such as greater distance & multi drop installations,
large data format and a variety of baud rates (or communication speeds) so it accommodates biometrics without Ethernet or a PoE connection,
and remote updates from the panel

## Slide 9: Why OSDP?
Improved interoperability
- Certified IEC industry standard since 2020 (IEC EC 60839-11-5)
OSDP Verified program helps ensure interoperability
SIA training courses
PSIA’s Public Key Open Credential specification now supports OSDP
Notes: Wiegand was a boon when it became the de facto standard, so to replace Wiegand with another protocol, OSDP also needs interoperability
SIA adopted OSDP as its official industry standard and OSDP completed IEC certification in 2020
OSDP Verified program helps ensure interoperability although we always recommend bench-testing items together before installing in the field
The Physical Security Interoperability Alliance (PSIA) today announced its Public Key Open Credential (PKOC) specification has expanded to support Open Supervised Device Protocol (OSDP). The new specification, PKOC over OSDP version 1.63, was unanimously ratified by the PSIA Board on March 22. It demonstrates how the ecosystem for PKOC, an open and freely available specification, can be extended to support a range of access control use cases.

## Slide 10: Comparison of OSDP and Wiegand Wiring
Wiegand
( Strobed, F2F, Serial )
Notes: Share details of a case study - John?

## Slide 11: Comparison of OSDP and Wiegand Wiring
Wiegand
OSDP
Notes: Share details of a case study - John?

## Slide 12: Major Differences
Simplex vs. Half Duplex
Wiegand is one way unsupervised
Wiegand functionality is done via discrete signaling wires
Wiegand Vulnerability - no ability to secure the transmission
OSDP is bidirectional, fully supervised
OSDP functionality is done via commands / replies
OSDP can be encrypted and authenticated
Multi-Drop Topologies
Notes: Share details of a case study - John?

## Slide 13: Why OSDP?
Industry impact
- Hot Dog Stand
Fortune 500
Notes: Share details of a case study - John?

## Slide 14: OSDP Systems
Full systems vs. retrofits
OSDP
Wiegand
Notes: Installing OSDP may mean a brand-new system install, or a retrofit

## Slide 15: OSDP Systems
Retrofitting Wiegand system
Install new OSDP devices in existing Wiegand systems
Upgrade highest security areas with OSDP readers & converters
Cost & time savings but restricted to 1-to-1 expansion
Notes: 2. Retrofit Existing System
Securely connect new OSDP reader to existing Wiegand controllers using converters
Start with the highest security areas
Allows you to minimize costs since you can keep Wiegand controllers and potentially retaining existing cable, but be aware that the infrastructure generally supports 1-to-1 replacement, but not expanded number of readers or multi-drop installations

## Slide 16: OSDP Systems
Full OSDP systems
Takes full advantage of OSDP
Main system components all support OSDP
For new construction or when budget / timeframe support replacement
Notes: Full OSDP system is designed to take full advantage of OSDP capabilities, such as
a range of cable runs
multidrop OSDP buses
Planning to use OSDP I/O devices (DPS, REX switch, door strike, etc.) as they become available
For Full OSDP systems, the main system components must all support OSDP. This would include the access control panel, RFID readers, and cable runs
Especially suitable for new construction
and when there is the budget and timeframe to replace existing equipment and infrastructure
A full OSDP system is especially important for future expansion

## Slide 17: OSDP Components
OSDP panel (ACU) sourcing considerations
Maximum number of OSDP devices on single port (generally 1, 2, 4, 8)
How it supports I/O
Range of baud rates supported
Pairing mode for Secure Channel encryption
Configuring controller to poll each reader (multi-drop)
Notes: First primary system component is an OSDP panel:
Often referred to as Access Control Unit (ACU)
Panel design considerations:
How many OSDP devices can be run on a single port, for multi-drop OSDP reader installations? (OSDP spec defines 126 unique device addresses, 0-126; in theory 32 would be a practical maximum based on timing and electrical considerations; generally you’ll be choosing from OSDP controllers that support 1, 2, 4, or 8 OSDP readers on a single OSDP port)
How does it support OSDP I/O devices?
Is the full range of baud rates supported (communication speeds)? If not the full range, which ones?
Does the panel support a pairing mode for setting up Secure Channel encryption, or does the manufacturer prescribe another method of pairing OSDP devices?

## Slide 18: OSDP Components
OSDP reader (PD) sourcing consideration
Default configuration
Configuring address/baud rate for each reader
Secure Channel key management
Factory default process
Notes: OSDP Readers
Often referred to as Peripheral Devices (PDs)
In multi-drop configuration, must each be configured with a unique address and the same baud rate (communication speed).
OSDP access controller must be configured to poll each reader at its assigned address and to communicate at the same baud rate as the readers.
(?) Discuss setting up Secure Channel out of band?
May be securely connected with Wiegand panel using third-party converters
Expect to see other (non-reader) types of peripheral devices in the future
Factory default process - decommissioning

## Slide 19: OSDP Components
OSDP wire runs: Multi-drop vs. home-run systems
Notes: 3. OSDP wire runs & cable choices
Let’s talk about differences between multi-drop and home-run systems
Multi-drop runs are when readers are daisy-chained together, so just 1 wire run from the controller to the farthest reader
Home-run is when there is a separate wire run between each reader and the controller

## Slide 20
OSDP components
OSDP wire runs: Home-run
Wiegand wire in place
Wiegand wire: Works with 1 device at < 500 ft., at < 9600 baud
Not future-proof; best practice is to replace
Notes: Home-run systems
Common to use when adding OSDP to an existing site because each Wiegand reader is home-run, and often it is the Wiegand reader that is being replaced.
Wiegand wire is likely present and worked because it’s less than 500 ft., and is connected to one device at 9600 baud or less.
However it’s not future-proof —if you increase the speed, it will collapse at that point or cause intermittent problems that would be difficult to troubleshoot. It’s a best practice to replace the cable to ensure it will support the system in the future.

## Slide 21
OSDP components
Home-run wiring
Think Wiegand
Wiegand wire: Works with 1 device at < 500 ft., at < 9600 baud
Not future-proof; best practice is to replace
Notes: Home-run systems
Common to use when adding OSDP to an existing site because each Wiegand reader is home-run, and often it is the Wiegand reader that is being replaced.
Wiegand wire is likely present and worked because it’s less than 500 ft., and is connected to one device at 9600 baud or less.
However it’s not future-proof —if you increase the speed, it will collapse at that point or cause intermittent problems that would be difficult to troubleshoot. It’s a best practice to replace the cable to ensure it will support the system in the future.

## Slide 22
OSDP components
Multi-drop wiring
1 cable run supports multiple PDs
Bundled access control or OSDP-specific cable
Needed for new construction or full OSDP systems
Important! Correctly ID OSDP wires in bundled cable
Notes: Multi-drop systems
Can support entire set of doors on 1 cable at a range of up to 4,000 feet
Bundled access control cable, including OSDP-specific cable,
commonly contains power and communication for OSDP readers and door hardware. Convenience of all-in-one cable; no need to pull additional cable
Can be planned for new construction or when you are doing a full OSDP system upgrade, since it is better suited for long distances and multi-drop installations
Important to correctly identify the OSDP wires— Check with manufacturer
(take a length of cable to show in the ed session)

## Slide 23: OSDP Best Practices
Order of installation

## Slide 24: OSDP Best Practices
“Dead or Alive” demo

## Slide 25: OSDP Best Practices
Configuration
Know your tool options: Built-in, controller, or third-party
Preconfigure / test Secure Channel encryption key, device address, baud rate
Notes: Best practices with configuration
Know your tool options:
  Some manufacturers provide tools for configuring their devices
  Other devices rely on the OSDP access controller to send configuration commands
  There are also third-party tools, can use to configure device address, baud rate, and encryption keys, either on test bench or in the field
To save time and prevent troubleshooting headaches, preconfigure and bench-test Secure Channel encryption key, device address, and baud rate before arriving onsite.

## Slide 26: OSDP Best Practices
Device address: Required step in OSDP (different from Wiegand!)
Find default addresses of both reader & controller
Plan device addresses
Preconfigure and bench-test before installing
Notes: Best practices for device addresses
Note that setting the device address in the reader is a required step in OSDP installation, not found in Wiegand installation
There is no default address for OSDP readers/devices or OSDP access controllers in OSDP specification. Some manufacturers’ products default to address 0; some default to address 1.
For Home-run OSDP systems, the OSDP reader address must match address the OSDP port is configured to poll
For Multi-drop OSDP systems, each OSDP reader and OSDP device on the OSDP port requires a unique address.
Best practices:
Find default addresses of both reader and controller
Plan ahead how each device will be addressed to avoid installation issues with mismatching device addresses
  Avoid certain addresses if possible
  Addresses 0 and 1 are common default addresses
  Address 127 is the broadcast address and is not a valid address to set an OSDP reader/device to.
  Addresses at the upper end of the address space, near address 127, are likely to be used in the future for special functions.
Configure and test before installing

## Slide 27: OSDP Best Practices
Baud rate (reader-panel communication speed)
OSDP specification defines 6 rates; what does your device support?
Lower rates better to start (example: 9600)
Higher baud rate better for higher bandwidth needs (example: biometric)
Notes: Baud rate: Speed at which the OSDP readers and OSDP access controller communicate.
Six baud rates defined in OSDP specification: 9600, 19200, 38400, 57600, 115200, and 230400.
Check with manufacturer to know which baud rates are supported by device — Not all OSDP devices support every baud rate
Use of lower baud rates:
It is best to start with lower baud rates and only move to higher baud rates if necessary.
Lower baud rates support better data integrity, especially over long cable runs or over cable with low quality cable, such as cable with many splices.
If the cable supported Wiegand, it can likely support OSDP at 9600 baud.
Generally not much data transferred between OSDP devices (messages measures in bytes; not kilobytes or megabytes), with some exceptions.
Use of higher baud rates
To put the polling speeds at higher baud rates into perspective, an OSDP access controller polling 8 OSDP readers at 115200 baud completed 300 polls per second. Each of the 8 OSDP readers are polled approximately 38 times per second. In order to provide quick credential transactions for the user the reader only needs to be polled a few times per second.
Used for higher bandwidth functions supported by certain devices (files can be measured in megabytes, if the devices support files of that size)
OSDP File Transfer protocol (allows OSDP access controller to send a file to the OSDP reader/device; often used to send firmware updates to OSDP readers, but other uses as well)
Firmware updates
Biometric data (files can be significantly larger than RFID credential data, which typically tops out at 200 bits)

## Slide 28: OSDP Best Practices
Secure Channel encryption: CRITICAL to enable on every OSDP reader
Review manufacturer’s and 3rd party options
Always set up ‘out of band’
Key management
Notes: Enabling Secure Channel
Critical to enable Secure Channel on every OSDP reader in any system: Both Wiegand and unencrypted OSDP communication are susceptible to bad actors placing devices on the data lines and capturing credential information.
Always set up Secure Channel encryption “out of band”
Encryption key is sent to the OSDP reader/device with the Keyset command
Process:
Review manufacturer’s and third-party options for configuring encryption keys out of band. For example:
Connect OSDP reader with controller directly over a few feet of cable
Separately load encryption keys into OSDP access controller, and OSDP reader
Load key into OSDP access controller in the software
If provided, load key into OSDP reader with a manufacturer-provided tool such as mobile app over Bluetooth connection
Load key into OSDP reader with a third-party tool, such as a device that connects directly to the OSDP reader and sends the Keyset command
If automatic pairing mode is supported, OSDP reader and OSDP controller connect and automatically create and configure themselves with a random key.
Key management
Keys should not be known to anyone
Are the keys being stored after configuration for later use?
How are they being stored?
Are the keys being randomly generated, loaded into the OSDP devices, and then discarded?
Some encryption configuration methods to not disclose the key that is used, such as the automatic pairing mode
Restoring factory default
Because key may not be known, it is important to know how to factory default devices (restoring to a known state with a known encryption key)
Factory default can restore encryption key to the default key defined in the OSDP specification, or to a default key defined by the manufacturer.

## Slide 29: OSDP: The Tools
Secure Channel encryption: CRITICAL to enable on every OSDP reader
Review manufacturer’s and 3rd party options
Always set up ‘out of band’
Key management
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 30: You Can’t Fix What You Can’t See
No instructions
No measurements
Lack of experience
No built-in indicators
Misinterpretation
Incompatibility
Improper configuration
Improper Installation
Edge case
The White Wire should be here
Problem
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 31: Trace Tools
You have to see what the electrons are up to (is the reader communicating?)
Built-In Tracing ( PACS, ACU )
OSDP Trace Tool
Export to common file
Send to the “experts”
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 32: Communication Parameter Settings
Built-In ( PACS, ACU, PD )
3rd Part Tools
Laptop and RS-485 Adaptor
Smart phone with USB-C to RS-485
Dedicated Configuration Tools
Open source tools using Linux
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 33: OSDP Bench-Testing Tools
Bench Testing
Field Testing
Development
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 34: Logic Analyzer / Oscilloscope
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 35: Demonstration
View OSDP communication using logic analyzer
View OSDP communication using Trace Tool
Set OSDP Communication Parameters using dedicated tool
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 36: Vendors
Access Control System suppliers
Card Reader and Peripheral manufacturers
Cypress Integration Solutions
ID Machines
Z-Bit (osdpworld.com)
Open Source - git hub, libosdp-conformance, osdpcap format
RasPi Platform
OSDP Bench - Android
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 37: Last, But Not Least
Future developments
- Current Specification is v2.2.1
- Roadmap for Version 2.3 is in process
  Enhancements for faster PIV
  Behavior Profiles
  Best Practices Guidelines
OSDP Verified Program
OSDP Boot Camp
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 38: Q & A
Thank You
Please scan and share your feedback
on this session in the SIA survey.
Notes: ? OSDP I/O devices, credentials, PIV?

## Slide 39
TITLE HERE
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.

## Slide 41
TITLE HERE
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.